## Slide 1: EE 445L – Embedded System Design Lab
Digital Communication
DAC speaker
Microphone ADC
Sound Energy

## Slide 2: Overview
Network
  Collection of interfaces
  Share a physical medium and data protocol
Decode -> transmit -> encode
  Energy, Signal to noise
Shannon channel capacity
  Theoretical Limit
Definitions
  Guided/unguided,
  Duplex (full/half/simplex),
  Bandwidth (many definitions)
  Diameter
SPI -full
Sclk
Fss
MOSI
MISO
UART -full
TxD
RxD

## Slide 3: Important issues
Line Coding
  bits as electronic/photonic signals
Modulation
  digital information represented with sinusoids
Error detection and correction
  channel coding techniques for improving transmission fidelity by adding data
Compression
  source coding removes redundant data
EE 445L – Bard, McDermott, Valvano

## Slide 4: Data rates
EE 445L – Bard, McDermott, Valvano

## Slide 5: Vocabulary
Transmitter (Tx)
Receiver (Rx)
Medium
  Guided medium
    e.g. twisted pair, optical fiber
  Unguided medium
    e.g. air, water, vacuum
EE 445L – Bard, McDermott, Valvano

## Slide 6: Vocabulary (cont.)
Simplex
  One direction
    e.g. Television
Half duplex
  Either direction, but only one way at a time
    e.g. police radio
(Full) Duplex
  Both directions at the same time
    e.g. telephone
EE 445L – Bard, McDermott, Valvano

## Slide 7: Vocabulary (cont.)
Analog (continuous) signal
  Varies continuously (infinite number of values) with time
Digital (discrete) signal
  Varies between a finite set of values with time
Periodic signal
  Signal repeats regularly with time
Aperiodic signal
  Signal does not repeat with time
EE 445L – Bard, McDermott, Valvano

## Slide 8: It is all about energy
How rapidly can information (bits) be communicated?
That depends upon:
  the amount of energy used in transmitting each signal
  the distance between transmitter and receiver – attenuation and distortion
  the amount of noise associated with the channel
  the bandwidth of the channel
EE 445L – Bard, McDermott, Valvano

## Slide 9: Bandwidth
Bandwidth – what do we mean?
  the problem is: strictly band-limited signals are not realizable, because they imply signals with infinite duration and duration-limited signals imply arbitrarily high frequencies (Sklar – Digital Communications)
EE 445L – Bard, McDermott, Valvano

## Slide 10: Bandwidth
EE 445L – Bard, McDermott, Valvano
Then bandwidth could be:
  half-power bandwidth –interval between frequencies at which Gx(f)* has dropped to half power (3dB)
    *power spectral density – the distribution of power across the frequency spectrum of the signal
  equivalent rectangular bandwidth – let Px be the total signal power over all frequencies, then Wn = Px/ Gx(fc)
  null to null bandwidth – frequency interval between first two nulls of Gx(f)
  fractional power containment bandwidth – bandwidth with 0.5% of signal power above and below the band (FCC)
  bounded power spectral density – band defined so that everywhere outside Gx(f) must have fallen to a given level
  absolute bandwidth – the interval that contains all of the signal’s frequencies (abstraction)

## Slide 11: Bandwidth
Definition: The bandwidth of a channel is the range of frequencies passed by the channel. (Leon-Garcia)
f
0
W
A(f)
Lowpass and idealized lowpass channel
0
W
A(f)
1
f
EE 445L – Bard, McDermott, Valvano

## Slide 12: Bandwidth
Assume a channel of bandwidth W (Hz) and consider positive and negative going pulses each carrying one bit of information, i.e., an amplitude of ‘A’ = ‘1’ and ‘-A’ = ‘0’
Maximum pulse transmission rate (Nyquist rate) is 2W pulses/second
Channel
t
t
-A
A
EE 445L – Bard, McDermott, Valvano

## Slide 13: I2C
0 encoded as 0V, E=0
1 encoded as hiZ (float) output I=0, E=0
Lower pullup resistor (increase I on high)

## Slide 14: Encoding
Proposed improvement:
  send pulses at the Nyquist rate
  vary pulse amplitude, e.g., {-A, -A/3, A/3, A corresponding to 00, 01, 10, 11}
  if M = 2m levels are employed, m bits are communicated with each pulse
    group of m bits is called a symbol
  our apparent information rate is then:
  r = 2*W*m bits/s
And, we can apparently select m to be as large as we’d like!
EE 445L – Bard, McDermott, Valvano

## Slide 15: Effect of noise on encoding
REALITY CHECK!
  we must address the issue of noise
signal
noise
signal + noise
t
t
t
SNR =
Average Signal Power
Average Noise Power
SNR (dB) = 10 log10 SNR
EE 445L – Bard, McDermott, Valvano

## Slide 16: Effect of noise on encoding
Relationship between noise and signal
4 signal levels
8 signal levels
typical noise
EE 445L – Bard, McDermott, Valvano
n
s

## Slide 17: Shannon Channel Capacity
Shannon channel capacity:
C = W log2 (1 + SNR) bits/s
Example: Telephone channel
  W = 3.4 kHz and SNR ~ 38 dB => SNR ~ 6310
  C = 3.4 kHz log2 (1 + 6310) = 3.4kHz x 12.62 b/s
  = 42.9 kb/s
EE 445L – Bard, McDermott, Valvano

## Slide 18: How far can I go?
An analog repeater assists in addressing some of the issues:
Source
Repeater
Destination
Repeater
Transmission segment
EE 445L – Bard, McDermott, Valvano

## Slide 19: Repeater
The amplifier increments energy in all components of the signal it receives in an attempt to address attenuation
  note that the noise components are also increased
The equalizer attempts to appropriately adjust the energy to compensate for the distortion that will be introduced in the next transmission segment
Attenuated & distorted signal
+
noise
Equalizer
Recovered signal
+
residual noise
Repeater
Amp.
EE 445L – Bard, McDermott, Valvano

## Slide 20: How far can I go?
EE 445L – Bard, Valvano
An interesting observation:
  as the signal passes from analog repeater to analog repeater noise is added on each segment
  the noise is amplified at each repeater
  the energy associated with the signal that represents the information is, at best, reproduced as the original transmitter value
  ultimately, the ratio of the information signal power to noise power, or signal to noise ratio (SNR) begins to approach zero
  the system has a finite useful diameter

## Slide 21: Why digital?
Digital repeater operation:
  Incoming signal is processed as before
  Output is processed to determine which of a finite set of possible values is represented by the incoming signal
  the value is selected and a new – noiseless and undistorted – signal is transmitted
  if the decision can’t be made an error condition results
Amplifier
Equalizer
Timing
Recovery
Decision Circuit.
& Signal
Regenerator
Digital Repeater
EE 445L – Bard, McDermott, Valvano

## Slide 22: Infinite diameter
The digital system:
  has superior fidelity because the components of its transmission system are aware of how the information is represented by the signals being carried
  can have an effective infinite diameter
    why?
EE 445L – Bard, McDermott, Valvano

## Slide 23: Analogy
EE 445L – Bard, McDermott, Valvano
Interesting observation:
  What is the difference in communicating information from location X to location Y and communicating the same information from time P to time Q?
  The same analysis and techniques that pertain to the spatial communication of information also apply to the temporal case.
  Storage systems, databases, archives can all benefit from the digital representation of the information that they contain.

## Slide 24: Digital communications
Digital technology
  Low cost ULSI technology
Data integrity
  Longer distances over lower quality lines
  Error Checking and Correction (ECC)
Capacity utilization
  High bandwidth links economical
  High degree of multiplexing easier with digital techniques
Security & Privacy
  Encryption
Integration
  Can treat analog and digital data similarly
EE 445L – Bard, McDermott, Valvano

## Slide 25: Summary
Network
  Collection of interfaces
  Share a physical medium and data protocol
Decode -> transmit -> encode
  Energy is transmitted
  Signal to noise is important
Shannon channel capacity
  C = W log2 (1 + SNR) bits/s
Definitions
  Guided/unguided,
  Duplex (full/half/simplex),
  Bandwidth (many definitions)
  Diameter
How does Data storage work?
Store a bit? Energy
Transmits energy across time